## Slide 1: Performance Evaluation of Knowledge-based Kitting via Simulation
Thomas Kramer1, Zeid Kootbally2, Stephen Balakirsky3, Craig Schlenoff4,
Anthony Pietromartire4, and Satyandra Gupta2
Presented by Zeid Kootbally
1: Department of Mechanical Engineering, Catholic University of America, Washington, DC, USA
2: Department of Mechanical Engineering, University of Maryland, College Park, MD, USA
3: Georgia Tech Research Institute, Atlanta, GA
4: Intelligent Systems Division, National Institute of Standards and Technology, Gaithersburg, MD, USA

## Slide 2
Process in which individually separate but related items are grouped, packaged, and supplied together as one unit
Utilized in many manufacturing assembly lines
Kitting (Kit Building)

## Slide 3
Process in which individually separate but related items are grouped, packaged, and supplied together as one unit
Utilized in many manufacturing assembly lines
Robotic solutions require
  Flexibility - Many parts with varying characteristics, part-to-part inconsistences
  Agility - Changes in part supply locations, lack of fixturing
  Rapid re-tasking – Ability to quickly build new varieties of kits
Kitting (Kit Building)

## Slide 4
Knowledge Driven Methodology

## Slide 5
Knowledge Driven Methodology
Domain Specific Information
Captures operational knowledge that is necessary to be successful in the particular domain in which the system is designed to operate
  Information on items ranging from
    From what actions and attributes are relevant,
    To what the necessary conditions are for an action to occur and what the likely results of the action are
  Formalism known as a state variable representation [1]
[1] D. Nau, M. Ghallab, and P. Traverso, Automated Planning: Theory & Practice. San Francisco, CA, USA: Morgan Kaufmann Publishers Inc., 2004.

## Slide 6
Knowledge Driven Methodology
Ontology

## Slide 7
A base ontology (OWL/XML Kitting) contains all of the basic information that was determined to be needed during the evaluation of the use cases and scenarios
Knowledge Driven Methodology
Ontology

## Slide 8
The OWL/XML SOAP ontology describes aspects of individual actions and predicates that are necessary for the domain under study
Knowledge Driven Methodology
Ontology

## Slide 9
  The instance files describe the initial and goal states for the system
    Initial state file must contain a description of the environment
    Goal state file only needs to contain information that is relevant to the end goal of the system
Knowledge Driven Methodology
Ontology

## Slide 10
Knowledge Driven Methodology
Planning Language

## Slide 11
Knowledge Driven Methodology
Planning Language
  Aspects of this knowledge are automatically extracted and encoded in a form that is optimized for a planning system to utilize (the Planning Language)
    Planning language used in the knowledge driven system is expressed with the Planning Domain Definition Language (PDDL) (version 3.0)
    The PDDL input format consists of two files that specify the domain and the problem

## Slide 12
Knowledge Driven Methodology
Planning Language
  Aspects of this knowledge are automatically extracted and encoded in a form that is optimized for a planning system to utilize (the Planning Language)
    Planning language used in the knowledge driven system is expressed with the Planning Domain Definition Language (PDDL) (version 3.0)
    The PDDL input format consists of two files that specify the domain and the problem
    Domain independent planning system used to produce a static Plan Instance File

## Slide 13
Knowledge Driven Methodology
Robot Language

## Slide 14
Knowledge Driven Methodology
Robot Language
The interpreter combines knowledge from the plan to form a set of sequential actions that the robot controller is able to execute
  Set written in a canonical robot command language (CRCL)
  CRCL provides generic commands that implement the functionality of typical industrial robots without being specific to
    The language of the planning system that makes a plan
    The language used by a robot controller that executes a plan

## Slide 15
Example of a CRCL file:
  InitCanon()
  SetLengthUnits("meter")
  SetAbsoluteSpeed(1.0)
  SetRelativeAcceleration(80.0)
  SetEndPointTolerance(0.002)
  SetIntermediatePointTolerance(0.01)
  OpenGripper()
  MoveThroughTo({ {{1.5,1,1}, {0,0,-1}, {1,0,0}},{{1.5,1,0.0001}, {0,0,-1}, {1,0,0}} }, 2)
  CloseGripper()
  EndCanon(2)
Knowledge Driven Methodology
Robot Language

## Slide 16
Simulates the execution of a plan (CRCL command file) for changing a kitting workstation from an initial state to a goal state
  Initial and goal states correspond to XML kitting schema
Built in C++ using OpenGL graphics
User controllable animated 3D view (pan, rotate, zoom)
Uses three windows: graphics, metrics, command & messages
Kitting Viewer

## Slide 17
Kitting Viewer

## Slide 18
Simulates the execution of a plan (CRCL command file) for changing a kitting workstation from an initial state to a goal state
  Initial and goal states correspond to XML kitting schema
Built in C++ using OpenGL graphics
User controllable animated 3D view (pan, rotate, zoom)
Uses three windows: graphics, metrics, command & messages
Two phases:
  (1) Execute commands
    Each push of ‘e’ key executes another command
  (2) Check final location of movable objects against goal state
    Each push of ‘e’ key checks another object
calculates execution metrics and a total score
Kitting Viewer

## Slide 19
The Kitting Viewer embodies a test method for comparing the performance of different kitting planning systems
It may be used to compare different plans for building kits
  Each plan to be compared has the same initial and goal states
Test Method

## Slide 20
Action Commands Executed Successfully
  Number of action commands that have been executed successfully so far
Other Commands Executed Successfully
  Number of commands that are not action commands that have been executed successfully so far – mostly setting commands
Total Robot Distance Moved (from command points)
  Total distance that the tool tip has moved so far
Total Execution Time (from speed and distance, not clock)
Range Errors (e.g., percentage > 100)
  Number of times a command tries to set a parameter to a value that is out of the allowed range of the parameter
Parse Errors
  Number of lines in the CRCL command file that cause an error in the command file parser
Gripper Use Errors (open or close when robot has no gripper)
Tool Change Errors (must be at tool changer)
Total Errors
Useless commands (e.g., open gripper when already open)
Metrics – Execution Phase

## Slide 21
Objects Located Correctly
  Number of movable goal objects checked so far that were moved from their initial location to the correct goal location
Object Location Errors
  Number of movable goal objects checked so far whose final position is not the one given in the goal file
Total Basic Goal Object Distance Moved
  Total net distance moved from initial location to final location by movable basic goal objects checked so far
Total Errors
  Number of Total Errors from the first phase plus the number of Object Location Errors for movable goal objects checked so far
Score (next slide)
Metrics – Check Phase

## Slide 22
Scoring is configurable using a scoring file to specify weights and (optionally) valuation functions for 5 factors
Five factors are:
  Right Stuff: a measure of achieving goal positions
  Command Execution: fraction of commands executed correctly
  Distance: a measure of robot efficiency in terms of distance
  Time: a measure of robot efficiency in terms of time
  Useless Commands: from 1st phase
Scoring file is XML instance file corresponding to XML schema for scoring kitting
Scoring

## Slide 23
Metrics for industrial kit building have been developed based on a knowledge model
A configurable method of computing a net score from the metrics has been developed
A Kitting Viewer has been developed that simulates the execution of a plan in the form of a robot command file intended to take a kitting workstation from an initial state to a goal state
The Kitting Viewer computes the metrics and a final score for the plan
Conclusion

## Slide 24
Allow identical parts in the goal file to be interchangeable
  If parts A and B are identical, and the goal file has part A in position 1 and part B in position 2, it will be equally valid to put part B in position 1 and part A in position 2
Other desirable improvements
  Using OWL instance files as input
  Implementing animation of gripper rotation
  Using other types of grippers
  Implementing kinematics of commercial robots
    Move towards ROS/USARSim framework
Future Work

## Slide 25
Scoring
Additive Score
Total Score