## Slide 1: Overview of Industrial Robot Group Activities
Dr. Stephen Balakirsky
National Institute of Standards and Technology
stephen@nist.gov

## Slide 2: Kit Building
Process in which individually separate but related items are grouped, packaged, and supplied together as one unit
Utilized in many manufacturing assembly lines
Robotic solution requires:
  Flexibility –Many parts with varying characteristics, part-to-part inconsistences
  Agility – Changes in part supply locations, lack of fixturing
  Rapid re-tasking – Ability to quickly build new varieties of kits

## Slide 3: Operational System
Video is 2x real time

## Slide 4: Planning Problem
Ƥ = (Ʃ, s0, g)
  Ʃ - State transition system (possible actions)
  S0 - Initial conditions (objects and relationships)
  g – Goal conditions
Initial Condition
Goal Condition
We would like to examine the knowledge requirements of this planning problem

## Slide 5: Underlying Knowledge Representation
Actions
  What actions and attributes are relevant
  Necessary conditions for an action to occur
  Likely results of the action
Objects
  What objects and attributes are relevant
  Taxonomy of objects
  Relationships between objects
Dynamic world
  Object attributes change over time
  Actions do not always accomplish what we want them to
Desire to maintain OWL compliance

## Slide 6: Limitations of OWL
Set of static files with no real-time information
  Can auto-generate MySQL database from OWL instance file and maintain database with sensor processing (access functions also auto-generated)
  Can automatically re-generate OWL instance file to allow for continued reasoning
No way to encode preconditions and effects of actions
  OWL Services (OWL-S) and the Semantic Web Rule Language (SWRL) are extensions that provide for actions with preconditions and effects
Image from mysql-workbench

## Slide 7: OWL-S Model
Requires generation of OWL-S syntax for rule, pre-conditions, and effects
Requires generation of SWRL (Semantic Web Rule Language) rules
Support issues with Protégé 4.2 plug-ins

## Slide 8: OWL/OWL-S Issues
Naïve user, but…
  SWRL Rules
    Very verbose data entry
    Difficult/impossible to represent negation
  OWL Instance Modification
    Open world assumption allows spelling errors
    Need to follow complex trail of tables and pointers
    Removal of instance requires careful clean-up to remove “hanging” entries
Is there another way?
  Investigated use of XML and PDDL with automatic generation of OWL files

## Slide 9: Ontology Design: Protégé View
OWL Viz view of KitDesign
  Arguably little or no useful information presented
  Is there a better way to visualize the representation?

## Slide 10: Data Entry – Protégé View
Required to navigate multiple tables
Required to add pointers from table to table
Required to typecast every data entry
  Is there a better way to perform data entry?

## Slide 11: Ontology Design
Clearly shows elements, element structure and properties, and classes

## Slide 12: Data Entry
Able to see all relevant fields for data entry
Strictly typecast

## Slide 13: XML Knowledge Representation
Preceding two slides1 were views into XML representation
We have created XML->OWL conversion tools
  Can automatically generate an OWL “instance” file from an XML file
  Work currently underway to generate OWL “class” file from XML schema
XML provides
  Closed world assumption
  Type checking
  Consistency checking
1Images created with XML Spy product. NIST does not endorse or recommend any commercial product.

## Slide 14: Back To SWRL: State-Variable Representation
Our real purpose in using OWL-S and SWRL is to encode actions, preconditions, effects, and plans
State-Variable Representation1 (SVR) used to formally define environment’s state and actions
  Each state is represented by a tuple of values of n state variables {x1,…, xn}
  Action is represented by a partial function that maps this tuple into some other tuple of values of the n state variables
1Dana Nau, Malik Ghallab, and Paolo Traverso. 2004. Automated Planning: Theory & Practice. Morgan Kaufmann Publishers Inc.

## Slide 15: Compose SVR in Planning Domain Definition Language (PDDL)
SVR is not a standard interchange language
  Can use the PDDL to encode the SVR
Entire kitting domain composed of:
  9 high-level operators: take-kit-tray, put-kit-tray, take-kit, put-kit, take-part, put-part, attach-eff, remove-eff, create-kit
  28 predicate expressions that act as preconditions or are acted upon during effects: rhold-empty, r-with-eff, kit-tray-location, worktable-empty, …

## Slide 16: Compose SVR in Planning Domain Definition Language (PDDL)
Initial Condition
Goal Condition
Goal Condition encoded as set of predicate expressions
Initial Condition encoded as set of predicate expressions
Plan necessary to move from initial predicates to goal predicates

## Slide 17: System Alternatives?
XML Schema, “Initial Condition”, “Goal Condition” files
Hand created
OWL “Domain”, “Initial Condition”, “Goal Condition” files
PDDL Domain, Problem files, code for predicate generation
Hand created
OWL “Domain”, “Initial Condition”, “Goal Condition” files
Auto-gen
MySQL database, PDDL plan file
Auto-gen
System Execution
OWL-S, SWRL Rule files
PDDL Domain, Problem files
MySQL database, PDDL plan file
System Execution

## Slide 18: Both Techniques Provide Agile System
Video is 2x real time